## Slide 1: Task Orchestration : Scheduling and Mapping on Multicore Systems
Course TBD
Lecture TBD
Term TBD

## Slide 2: Outline
Scheduling for parallel systems
  Load balancing
  Thread affinity
  Resource sharing
  Hardware threads (SMT)
  Multicore architecture
  Significance of the multicore paradigm shift

## Slide 3: Increase in Transistor Count
Moore’s
Law

## Slide 4: Increase in Performance
Chart: theoretical maximum performance (millions of operations per second)
| 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
Improvements in chip architecture | 16 | 16 | 40 | 60 | 100 | 120 | 120 | 180 | 180 | 2000 | 2000 | 3000 | 3000 | 12000 | 12000 | 70000 | 70000 | 90000 | 90000 | 90000 | 150000 | 150000 | 550000 | 550000 | 1200000
Increases in clock speed | 16 | 16 | 16 | 25 | 33 | 50 | 50 | 66 | 66 | 200 | 200 | 300 | 300 | 733 | 733 | 2000 | 3060 | 3060 | 3060 | 3060 | 3300 | 3300 | 3800 | 3800 | 3460
16 MHz
25 MHz
Full Speed Level 2 Cache
instruction pipeline
longer issue pipeline
double speed artihmetic
Image adapted from Scientific American, Feb 2005, “A Split at the Core”

## Slide 5: Increase in Power Density

## Slide 6: The Power Wall
Going with Moore’s Law results in too much heat dissipation and power consumption
Moore’s law still holds but does not seem to be economically viable
The multicore paradigm
  Put multiple simplified (and slower) processing cores on the same chip area
  Fewer transistors per cm2 implies less heat!

## Slide 7: Why is Multicore Such a Big Deal?
Chart: theoretical maximum performance (millions of operations per second)
| 1986.0 | 1987.0 | 1988.0 | 1989.0 | 1990.0 | 1991.0 | 1992.0 | 1993.0 | 1994.0 | 1995.0 | 1996.0 | 1997.0 | 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0
Improvements in chip architecture | 16 | 16 | 40 | 60 | 100 | 120 | 120 | 180 | 180 | 2000 | 2000 | 3000 | 3000 | 12000 | 12000 | 70000 | 70000 | 90000 | 90000 | 90000 | 150000 | 150000 | 550000 | 550000 | 1200000
Increases in clock speed | 16 | 16 | 16 | 25 | 33 | 50 | 50 | 66 | 66 | 200 | 200 | 300 | 300 | 733 | 733 | 2000 | 3060 | 3060 | 3060 | 3060 | 3300 | 3300 | 3800 | 3800 | 3460
16 MHz
25 MHz
Full Speed Level 2 Cache
instruction pipeline
longer issue pipeline
double speed arithmetic
more responsibility on software

## Slide 8: Why is Multicore Such a Big Deal?
Parallelism is mainstream
  “In future, all software will be parallel”
      - Andrew Chien, Intel CTO (many concur)
Parallelism no longer a matter of interest just for the HPC people
Need to find more programs to parallelize
Need to find more parallelism in existing parallel applications
Need to consider parallelism when writing any new program

## Slide 9: Why is Multicore Such a Big Deal?
Parallelism is Ubiquitous

## Slide 10: OS Role in the Multicore Era
There are several considerations for multicore operating systems
  Scalability
  Sharing and contention of resources
  Non-uniform communication latency
Biggest challenge is in scheduling of threads across the system

## Slide 11: Scheduling Goals
Most of the goals don’t change when scheduling for multicore or multi-processor systems
Still care about
  CPU utilization
  Throughput
  Turnaround time
  Wait time
  Fairness
definitions may become more complex

## Slide 12: Scheduling Goals for Multicore Systems
Multicore systems give rise to a new set of goals for the OS scheduler
  Load balancing
  Resource sharing
  Energy usage and power consumption

## Slide 13: Single CPU Scheduler Overview
CPU
Ready Queue
I/O
Queue
Long-term Queue

## Slide 14: Multicore Scheduler Overview I
Core 0
Common
Ready Queue
Common
I/O
Queue
Long-term Queue
Core 1
Core 2
Core 3
Cores sharing the same short-term queues

## Slide 15: Multicore Scheduler Overview II
Long-term Queue
Cores with individual ready queues
Core 0
Ready Queue
I/O
Queue
end
Core 1
Ready Queue
I/O
Queue
end
Core 3
Ready Queue
I/O
Queue
end
Core 2
Ready Queue
I/O
Queue
end
No special handling required for many of the single CPU scheduling algorithms

## Slide 16: Load Balancing
Goal is to distribute tasks across all cores on the system such that CPU and other resources are utilized evenly
A load-balanced system will generally lead to higher throughput
Chart: Load averag (%) over k time slices
| core 0 | core 1 | core 2 | core 3
 | 15 | 98 | 21 | 20
Chart: Load averag (%) over k time slices
| core 0 | core 1 | core 2 | core 3
 | 40 | 33 | 40 | 40
BAD
GOOD
Scenario 1
Scenario 2

## Slide 17: The OS as a Load Balancer
Main strategy
  Identify metric for balanced load
    average number of processes waiting in ready queues
    (aka load average)
  Track load balance metric
    probe ready queues
    uptime and who utilities
  Migrate threads if a core exhibits a high average load
    If load average for cores 0-3 is 2, 3, 1, and 17 then move threads from core3 to core 2

## Slide 18: Thread Migration
The process of moving a thread from one ready queue to another is known as thread migration
Operating systems implement two types of thread migration mechanism
  Push migration
    Run a separate process that will migrate a thread from one core to another
    May be integrated within the kernel as well
  Pull migration (aka work stealing)
    Each core fetches threads from other cores

## Slide 19: Complex Load Balancing Issues
Chart: time
| Core 3 (t3) | Core 2 (t2) | Core 1 (t1) | Core 0 (t0)
CPU Time | 15 | 30 | 100 | 25
Idle Time | 85 | 70 | 0 | 75
Does it help to load balance this workload?
Will it make a difference in performance?
Thread migration or load balancing will only help with overall performance if t1 runs faster when moved to core0, core2 or core3
Assume only one thread executing on each core

## Slide 20: Load Balancing for Power
Chart: time
| Core 3 (t3) | Core 2 (t2) | Core 1 (t1) | Core 0 (t0)
CPU Time | 15 | 30 | 100 | 25
Idle Time | 85 | 70 | 0 | 75
This unbalanced workload can have huge implications for power consumption
P = cv2f and P t
One core running at a higher frequency than the others may result in more heat dissipation and overall increased power consumption
Power consumption is tied to how fast a processor is running
P = power, f = frequency,
c = static power dissipation
v = voltage and t = temperature

## Slide 21: Load Balancing for Power
Chart: time
| Core 3 (t3) | Core 2 (t2) | Core 1 (t1) | Core 0 (t0)
CPU Time | 15 | 30 | 100 | 25
Idle Time | 85 | 70 | 0 | 75
Operating Systems are incorporating power metrics in thread migration and load balancing decisions
Achieve power-balance by eliminating hotspots
Can also try to change the frequency
  AMD Powernow, Intel Sidestep
    Can utilize hardware performance counters
  core utilization
  core temperature
Linux implements this type of scheduling
  sched_mc_power_savings

## Slide 22: Load Balancing Trade-offs
Thread migration may involve multiple context switch on more than one core
Context switches can be very expensive
Potential gains from load balancing must be weighed against the increased cost from context switches
Load balancing policy may conflict with CFS scheduling
  balanced load does not imply fair sharing of resources

## Slide 23: Resource Sharing
Current multicore and SMT systems share resources at various levels
OS needs to be aware of resource utilization in making scheduling decisions

## Slide 24: Thread Affinity
Tendency for a process to run on a given core for as long as possible without being migrated to a different core
  aka CPU affinity and processor affinity
The operating system uses the notion of thread affinity in performing resource-aware scheduling on multicore systems
If a thread has affinity for a specific core (or core group) then priority should be given to schedule the map and schedule the thread to that specific core (or group)
Current approach is to use thread affinity to address skewed workloads
  Start with default (all cores)
  Set affinity of task I to core j if core j is deemed underutilized

## Slide 25: Adjusting Thread Affinity
Linux kernel maintains the task_struct data structure for every process in the system
Affinity information is stored as a bitmask in the cpus_allowed field
Can modify or retrieve the affinity of a thread from user-space
  sched_setaffinity(), sched_getaffinity()
  pthread_setaffinity_np(), pthread_getaffinity_np()
  taskset
demo

## Slide 26: Thread Affinity in the Linux Kernel
/* Look for allowed, online CPU in same node. */
for_each_cpu_and(dest_cpu, nodemask, cpu_active_mask)
if (cpumask_test_cpu(dest_cpu, &p->cpus_allowed))
return dest_cpu;
/* Any allowed, online CPU? */
dest_cpu = cpumask_any_and(&p->cpus_allowed, cpu_active_mask);
if (dest_cpu < nr_cpu_ids)
return dest_cpu;
/* No more Mr. Nice Guy. */
if (unlikely(dest_cpu >= nr_cpu_ids)) {
dest_cpu = cpuset_cpus_allowed_fallback(p);
/*
* Don't tell them about moving exiting tasks or
* kernel threads (both mm NULL), since they never
* leave kernel.
*/
if (p->mm && printk_ratelimit()) {
printk(KERN_INFO "process %d (%s) no "
"longer affine to cpu%d\n",
task_pid_nr(p), p->comm, cpu);
}
}
Linux kernel 2.6.37, sched.c

## Slide 27: Affinity Based Scheduling
Affinity based scheduling can be performed under different criteria, using different heuristics
Assume 4 cores with two L2 shared between core 0 and core 1, core 2 and core 3, L3 shared among all cores
Core 0
Core 1
Core 2
Core 3
L1
L1
L1
L1
L2
L3
L2

## Slide 28: Affinity Based Scheduling
Scheduling for data locality in L2
  A thread ti that shares data with tj should be placed in the same affinity group
  Can lead to unbalanced ready-queues but improved memory performance
C
P
Shared
Data in L2
P
C
time
reuse of data
reuse of data
reuse of data

## Slide 29: Affinity Based Scheduling
Core 0
Core 1
Core 2
Core 3
L1
L1
L1
L1
L2
L3
L2
Core 0
Core 1
Core 2
Core 3
L1
L1
L1
L1
L2
L3
L2
P
C
P
C
Poor schedule for producer-consumer program
Good schedule for producer-consumer program
C
P
P
C

## Slide 30: Affinity Based Scheduling
Scheduling for better cache utilization
  Thread ti and tj only utilize 10% of the cache, tp and tq each demand 80% of the cache
  Schedule ti and tp on core 0 and core 1, tj and tq on core 2 and core 3
  May lead to loss of locality
Core 0
Core 1
Core 2
Core 3
L1
L1
L1
L1
L2
L3
L2
ti
tj
tp
tq

## Slide 31: Affinity Based Scheduling
Scheduling for better power management
  ti and tj are CPU-bound while tp and tq are memory-bound
  Schedule ti and tp on core 0 and tj and tq to core 2
Core 0
Core 1
Core 2
Core 3
L1
L1
L1
L1
L2
L3
L2
ti + tp
tj + tq

## Slide 32: Gang Scheduling
Two-step scheduling process
  Identify a set (or gang) of threads to and adjust affinity for them to execute in a specific core group
    Gang formation can be done based on resource utilization and sharing
  Suspend the threads in a gang to let one job have dedicated access to the resources for a configured period of time
Traditionally used for MPI programs running on high-performance clusters
Becoming mainstream for multicore architectures
  Patches available that integrates gang scheduling with CFS in Linux